## Slide 1: Network Protocols

## Slide 2: What is a Network?
A network is a way to transfer information or goods between people, places, or things.
1

## Slide 3: Computer Networking
Connecting devices together to share data
  Switch: links devices together to form a network
  Router: connects networks together and acts as a dispatcher
  Some devices act as both switch and router (many of the consumer-grade routers, for example)
2
IP Telephony Network Topology Diagram Example (Cisco)

## Slide 4: How does it work?
3

## Slide 5: A Simple View
Transport
Internet
Link
Application
Transport
Internet
Link
Application
HTTP
TCP
HTTP
IP
TCP
HTTP
Ethernet
IP
TCP
HTTP
HTTP
TCP
HTTP
IP
TCP
HTTP
Ethernet
IP
TCP
HTTP
IP
IP?
messages
Notes: Wrapper
HTTP, TCP, DNS

## Slide 6: Messages
Transport
Internet
Link
Application
HTTP
TCP
HTTP
IP
TCP
HTTP
Ethernet
IP
TCP
HTTP
message, data
segment, datagram
packet
frame
All are “messages”.
All are frequently referred to as “packets” (and for the purposes of this class, that’s ok).

## Slide 7: Web Browsing
Transport
Internet
Link
Application
Transport
Internet
Link
Application
1. TCP three-way-handshake: establish a connection
1. SYN
2. SYN+ACK
3. ACK
client
server
Note: There’s a DNS lookup of hostname over UDP...
TCP
TCP
IP
IP
MAC
MAC

## Slide 8: Web Browsing
Transport
Internet
Link
Application
Transport
Internet
Link
Application
TCP
TCP
2. Use the HTTP protocol to get a web page (and we’ll make further requests for all its resources, too)
IP
IP
HTTP GET Request
apache web server
HTTP Response
ESTABLISHED
ESTABLISHED
MAC
:80
client
server
MAC

## Slide 9: Skype
Transport
Internet
Link
Application
Transport
Internet
Link
Application
peer
peer
5
P2P VOIP
1. Connects to the login
server (TCP) – (all TCP
connections require the
three-way handshake)
2. Connects to a super node (TCP) So calls can be relayed behind firewalls. See http://www.theregister.co.uk/2003/10/08/how_does_skype_get_through/
3. Can use both
TCP and UDP
during calls.
If both Skype Clients are
public, messages are passed via UDP.
UDP
UDP
IP
IP

## Slide 10: What is a Protocol?
A protocol is a set of rules
“A set of conventions governing the treatment and especially the formatting of data in an electronic communications system.” Merriam-Webster Dictionary
Already we've named:
  HTTP, DNS, TCP, UDP, IP, and Ethernet protocols

## Slide 11: HTTP Protocol
Let’s look at an HTTP request / response cycle:
  Open Firefox, and visit http://www.facebook.com (or any site of your choosing)
  Select “Tools  Page Info” from the menu bar
  Select “Headers” to see the Request and Response headers

## Slide 12: HTTP Protocol
Let’s look at an HTTP request / response cycle:
  Open Chrome, and visit http://www.facebook.com (or any site of your choosing)
  Select (Hotdog menu)  Tools
   Developer Tools
  Select Network and then select a
  page (in this case www.facebook.com)
  Select “Headers” to see the Request and Response headers

## Slide 13: Network Models and the Internet Protocol Suite (TCP/IP)

## Slide 14: Network Models
Session
Transport
Network
Data Link
Physical
OSI 7-Layer reference model
Presentation
1
2
3
4
5
6
7
Application
Internet Protocol Suite
(also known as TCP/IP)
Transport
Internet
Link
Application
Protocol Examples
TCP, UDP...
IP (v4, v6)...
Ethernet, IEEE 802.11, USB, DSL...
NIC, Category 5 cables, Microwave
HTTP, FTP, IMAP, POP, SSH...
RFC 1122
http://tools.ietf.org/html/rfc1122

## Slide 15: Web Browsing
Transport
Internet
Link
Application
Transport
Internet
Link
Application
TCP
TCP
Revisited
IP
IP
HTTP GET Request
apache web server
HTTP Response
ESTABLISHED
ESTABLISHED
MAC
:80
client
server
MAC

## Slide 16: The Link Layer
Transport
Internet
Link
Application

## Slide 17: Link Layer
Physical layer
  Primarily Cat 5 (wired) and Microwave (wireless)
  Transmits and receives signals in the form of electrical current, light pulses, microwaves, etc.
Data link layer
  The Data layer converts the signal from the Physical layer into 1s and 0s that can be used by the Network layer (and vice versa)
  Ethernet is the most common data layer protocol
  Data layer messages (called frames) can only send messages on the local network
Transport
Internet
Data Link
Physical
Application

## Slide 18: Ethernet: Addressing
Every Ethernet adapter must have a unique address:
  Media Access Control (MAC) address
    aka physical address, Ethernet address, adaptor address, or hardware address (Saunders)
    is unique to a specific Ethernet adapter
    12-digit (48 bit) hexadecimal address
      e.g. 00-13-CE-BE-8B-9F
      Note: 64 bit MAC addresses will supersede 48 bit addresses due to address exhaustion
    The first 6 digits are the Vendor code, (0013CE belongs to Intel), the last 6 are the individual interface’s own. (Saunders)
      See http://coffer.com/mac_find/ to look up some vendor codes.

## Slide 19: Ethernet Communication 1 of 2
If one machine on an Ethernet Local Area Network wants to communicate with another, it sends a “broadcast” frame
All machines on the wire see the frame
  Check the destination address - is it me?
    yes - hand data up the stack
    no - ignore (or so we hope...)
  When the recipient responds, it will include it’s MAC address in the frame headers
  From this point, sender and receiver know each other by MAC address (no more broadcasts until a set period of time has passed)
Transport
Internet
Link
Application

## Slide 20: Ethernet Communication 2 of 2
Sender constructs a frame
  header includes source and destination address
  payload (data) comes from higher layer
Sender puts the frame on “the wire”
  asks physical layer to send it
Transport
Internet
Link
Application
frame
footer
header
higher layer data
payload

## Slide 21: The Internet Layer
Called the “Network Layer” in the OSI Reference Model
Transport
Internet
Link
Application

## Slide 22: Internet Layer
When you link computers up via the Link Layer you get a network.
When you link networks up, you get an internetwork.
You need the Network layer to get data between all the little networks (often called subnets) of your internetwork. (Saunders)
Transport
Internet
Link
Application

## Slide 23: Internet Protocol (IP)
The Internet Protocol (IP) is the Network layer protocol used on the Internet! It’s so handy that most everyone uses it on all their networks big and small.
Designed for huge, ever-expanding networks of networks. Works pretty well with unreliable links, routes can be re-built when links go down. Saunders, Drew. Introduction to Networking [PDF Document]. Retrieved from http://www.stanford.edu/dept/its/support/techtraining/techbriefing-media/Intro_Net_91407.ppt Used with permission of the author.
Transport
Internet
Link
Application

## Slide 24: IP Address (IPv4)
IP Address:
  First byte(s) identify the network
  Last byte(s) identify the machine
RPI is a Class B network
  128.113.subnet.host
Every host must have a unique IP address
Examples:
  128.113.91.241
  173.194.33.104
Class A | Net ID | Host ID |  | 
Class B | Network ID |  | Host ID | 
Class C | Network ID |  |  | Host ID
 | 8 bits | 8 bits | 8 bits | 8 bits

## Slide 25: Dotted Decimal Notation
IPv4 addresses are typically displayed by showing the value of each byte (in decimal).
Binary | Dotted Decimal
00000001 00000010 00000011 00000100 | 1.2.3.4
10000000 11010101 00000001 00000001 | 128.213.1.1
01111111 00000000 00000000 00000001 | 127.0.0.1 (localhost)

## Slide 26: IPv6
IPv4 addresses are 4 bytes (32 bits)
  Supports 232 (approximately 4.3 billion) addresses
  These are becoming exhausted
IPv6 addresses are 16 bytes (128 bits)
  Supports 2128 (approximately 340 undecillion) addresses
  Notation uses hexidecimal representing pairs of bytes separated by a colon. For example: 2620:0:2820:2:3c7f:8f2:389a:b053
How big is 340 undecillion?
    If you were to line up 340 undecillion soccer balls back-to-back on a string, the strand would wrap around our known universe 200 billion times.
    IPv6 .340 Undecillion Soccer Balls. [Web log posting]. Retrieved August 31, 2011 from http://www.ipv6resource.com/340-undecillion-soccer-balls.html

## Slide 27: IP Routing 1of 3
How do we communicate between machines when all we may have is an IP address??
ARP: Address Resolution Protocol
  Turns an IP address into a MAC address. You ask “Who’s 172.19.4.15” and if you get a reply, associate the MAC address with the IP address in your ARP table, and now you can keep sending your data to the intended recipient via the correct MAC address. (Saunders)
Every IP number not on your local network will “belong” to your router in your ARP table.
Transport
Network
Link
Application
ARP

## Slide 28: IP Routing 2 of 3
Routers keep a table of networks attainable by the router, called a “routing table”
A routing table keeps track of
  the topology of the network immediately around it,
  measurements to determine best paths to destination networks it knows about,
  and contains a “default route” for everything else.
Transport
Network
Link
Application

## Slide 29: IP Routing 3 of 3
When an Ethernet frame arrives at a router, it looks at the destination IP address inside the Internet packet and sends a new Ethernet (or other link layer) frame out the correct interface based on the routing tables.
That frame may go to the final host if it’s on one of the routers directly connected networks, or to another router, which does the same process, until your packet gets to the router responsible for that local network, who then sends your packet to the intended host.
Transport
Internet
Link
Application

## Slide 30: The Transport Layer
Transport
Internet
Link
Application

## Slide 31: Transport Layer 1 of 2
Responsible for delivering data to the application layer and for preparing application layer data for transport to other hosts
Breaks the data up into packets - usually called segments
Includes source and destination port numbers for application layer processes in its headers
Transport
Internet
Link
Application

## Slide 32: Transport Layer 2 of 2
Transmission Control Protocol (TCP)
  Guarantees reliability and sequencing
  Connection-oriented transmission
  Used by HTTP, FTP, SSH, Email
User Datagram Protocol (UDP)
  Does not guarantee reliability or sequencing
  Connectionless, best-effort transmission
  Used by VOIP, DNS, RTP where speed is more important than lost or damaged packets
Both use port numbers to identify processes
  e.g. http is often on port 80, https is often on port 443, mysql is often on port 3306, etc.
Transport
Internet
Link
Application
Notes: TCP – Mom calls you on your cell phone to come home for dinner
UDP – Mom shouts out the front door

## Slide 33: Sequencing
Different packets may take different routes to get to their destination
TCP has to put things back in order, UDP does not (though an application may try to do so, e.g. while buffering video)
Transport
Internet
Link
Application

## Slide 34: Ports 1 of 2
Ports are application or process-specific endpoints for data communication
Source and destination ports are included in the transport layer headers
Transport
Application
Process
Process
Process
Process
Process
ports
ports
ports
Transport
Internet
Link
Application

## Slide 35: Ports 2 of 2
Port numbers less than 1024 are typically reserved for important network services
Common well-known port numbers include 80 (HTTP), 443 (HTTP over TLS/SSL), 53 (DNS) etc.
You’ll sometimes see port numbers on URLs, e.g. “http://somesite:8080”
Transport
Internet
Link
Application

## Slide 36: The Application Layer

## Slide 37: Application Layer
HTTP
  Hypertext Transfer Protocol for the WWW
POP, IMAP
  Post Office Protocol and Internet Message Access Protocol for reading email
SMTP
  Simple Mail Transfer Protocol for sending email
DNS
  Protocol for the Domain Name System (both are referred to as “DNS”)
RTP
  Real-time Transport Protocol for delivering audio and video (e.g. VOIP – uses RTP over UDP)
Many more...
Transport
Internet
Link
Application

## Slide 38: Application Layer Example: DNS
Domain Name System

## Slide 39: Domain Name System
Domain Name System (DNS)
  It’s hard to remember IP addresses
  Since computers require numbers, DNS provides a lookup service to convert domain names to IP addresses
  Example:
    If you want the number for a host name within the rpi.edu domain, you’ll ask one of our DNS servers to give it to you. If you need to go outside rpi.edu, you’ll still ask our servers, but they’ll figure out which other server(s) should get your request, send it to them (unless our server has already cached it), and will send the reply back to you.

## Slide 40: Domain Name Hierarchy
other TLDs, e.g. net / gov / mil / etc...
com
edu
org
rpi
m
www
managed by Rensselaer
managed by IANA: Internet Assigned
Numbers Authority*
*IANA is part of ICANN: the Internet Corporation For Assigned Names and Numbers

## Slide 41: 2011: TLDs for Sale
June 2011: ICANN, the "Internet Corporation for Assigned Names and Numbers", approves a plan to allow groups to create new generic top level domains http://www.icann.org/en/announcements/announcement-20jun11-en.htm
Becoming a registrar is somewhat expensive:
    $185K evaluation fee
    Can take up to 20 months to go through evaluation
    $25K per year if approved (plus possible other fees)

## Slide 42: Suggested Reading
Designing for Cisco Internetwork Solutions, Chapter 1. Network Fundamentals Review.
  http://opac.lib.rpi.edu/search/t?SEARCH=Designing%20for%20Cisco%20Internetwork%20Solutions&searchscope=1

## Slide 43
Works Cited
Saunders, Drew. Introduction to Networking [PDF Document]. Retrieved from http://www.stanford.edu/dept/its/support/techtraining/techbriefing-media/Intro_Net_91407.ppt Used with permission of the author.
IPv6 .340 Undecillion Soccer Balls. [Web log posting]. Retrieved August 31, 2011 from http://www.ipv6resource.com/340-undecillion-soccer-balls.html
List of Figures
How were the messages sent along the wall? [Photograph, Great Wall of China]. Retrieved August 4, 2010 from http://www.visitourchina.com/china_great_wall/faq_02.htm
IP Telephony Network Topology Diagram Example [Bitmap]. Retrieved August 31, 2011 from http://www.cisco.com/iam/unified/ipt1/Preparing_Your_Network_for_Troubleshooting_and_Recovery.htm
Google Logo [Bitmap]. Retrieved September 3, 2010 from http://www.google.com
Slides 7 & 8: Cisco ASR 1000 Series Aggregation Services Routers [Photograph]. Retrieved September 5, 2010 from http://www.cisco.com/en/US/products/ps9343/prod_view_selector.html Cisco WS-C3750-48PS-S Catalyst 3750-48PS SMI Network Switch - 48-Port, 10/100, PoE [Photograph]. Retrieved September 5, 2010 from http://images.highspeedbackbone.net/skuimages/large/C94-2196-main.jpg
Baset, Salman A. and Henning Schulzrinne. (2004). An Analysis of the Skype Peer-to-Peer Internet Telephony Protocol [PDF Document]. Retrived from http://arxiv.org/ftp/cs/papers/0412/0412017.pdf [Untitled photo of iPhone with Skype]. Retrieved September 5, 2010 from http://static.skattertech.com/media/2010/05/skype-mobile-for-iphone-3g-600x342.jpg